## Slide 1
IOT BASED ECG
MONITOR
Kuiyu DING - 62716
Fahadh Mohamed JAHEER HUSSAN - 62720
Nuhu BELLO - 62713
Muhammad Arshad Shamshudeen AHMED - 62708

## Slide 2
TABLE OF CONTENT
1.Introduction
2.ECG sensor integration
3.Data processing
4.Data storage
5.Mobile application -- Flutter
  AD8232 ECG Sensor
  Connect sensor to Arduino
  MQTT
  BUFFER
  R-PEAK DETECTION--Neurokit2
  MongoDB Atlas
  PHYSIONET
  Live ECG data
  Alarm
  Historical data
Context , Architecture

## Slide 3
live ECG data
INTRODUCTION
In the IoT world, healthcare and technology combine to enable real-time health monitoring, and all data can be used for health tracking, early detection of cardiac abnormalities, and more.
Working flow:
Front end
Back end
Using Arduino-ECG sensor pairing and MQTT for efficient data flow
Using a specialized R peak detection algorithm to gain accurate bpm value
Cloud-based database stored historical ECG data
Alarm
Storage data

## Slide 4
ECG sensor integration
AD8232 ECG Sensor and Arduino
The AD8232 is an integrated signal conditioning block for ECG it acts as an operational amplifier to extract clear signal during PR and QT interval of the heartbeat.
Place ECG Sensor on Body and link to arduino.
value on serial monitor and the image on serial plotter
The closer to the heart the pads are, the better the measurement

## Slide 5
DATA PROCESSING

## Slide 6
MQTT
MQTT, which stands for MQ Telemetry Transport, is a lightweight messaging protocol for the Internet of Things (IoT) and machine-to-machine communication.
MQTT uses a publish/subscribe model, the Arduino publishes ECG data to a topic, which is then transmitted to a central broker. The Raspberry Pi subscribes to this topic, enabling it to receive and process the ECG data from the Arduino.
Mosquitto Broker

## Slide 7
BUFFER
After getting the data from MQTT protocol, The buffer is a Python list used to store a 500 ECG samples. As new ECG data is received, it is appended to the buffer, and when the buffer reaches its maximum length, processing is triggered.

## Slide 8
NeuroKit2 is a Python library designed for physiological signal processing and analysis, including electrocardiography (ECG), electrodermal activity (EDA), and electromyography (EMG). The ECG data is sampled at a rate of 22Hz.
NEUROKIT2
ecg_peaks function from NeuroKit2 is utilized to detect R-peaks in the ECG signal (method = "pantompkins1985")
ecg_rate function from NeuroKit2 is used to calculate heart rate (BPM)

## Slide 9
R-PEAK DETECTION

## Slide 10
DATA STORAGE

## Slide 11
PHYSIONET
- Used PhysioNet for ECG Signal Data
- Employed wfdb Library on Raspberry Pi for Data Retrieval
- Created 5000-sample Buffer for ECG Signal Storage
- Used NeuroKit Library to Detect R-peaks
- Calculated Heart Rate (bpm) from Identified R-peaks

## Slide 12
WEBSOCKET
Communication Protocol for Real-time Bidirectional Data Exchange
- Persistent Connection for Continuous Message Transmission
- Efficient and Low-latency Communication
- Commonly Used in Web Applications for Real-time Features
- Applications include Chat, Live Notifications, and Interactive Gaming
- Facilitates Transmission of Processed Data to MongoDB Atlas Database

## Slide 13
MONGODB
- Flexibility and Scalability
- JSON-like Document Storage
- Designed for Large Data Volumes
- Index Support and Replication
- Horizontal Scaling through Sharding
- Versatility in Applications
- Language and Platform Support

## Slide 14
MONGODB ATLAS
MongoDB Atlas simplifies database management in the cloud with automated scaling, security measures, and monitoring. In our project, 500 ECG samples, along with R-peaks and BPM, are sent to MongoDB Atlas using the connection string and viewed in mongodb compass

## Slide 15
R-PEAK

## Slide 16
MOBILE APPLICATION

## Slide 17
FLUTTER
Flutter is an open-source UI software development toolkit created by Google, designed for building natively compiled applications for mobile, web, and desktop from a single codebase

## Slide 18
The Mobile Application consists of Three main parts:
  Live ECG Data
  Alarm
  History
We have developed a mobile application using Flutter to visualize and interact with the ECG data.
Mobile Application
ECG

## Slide 19
LIVE ECG DATA
The Flutter application receives and processes this real-time data through the MQTT client

## Slide 20
ALARM
The BPM data stored in the database are visually alerts users if the BPM falls below 60 or exceeds 100. This visual indication uses colours, showing red for abnormal BPM values and green for normal ones.

## Slide 21
HISTORY
The Storage part of the application retrieves stored ECG samples from MongoDB Atlas using the MongoDB connection string. It allows users to view the ECG signal in graphical form, presenting images of the signal for the last 500 samples stored in the buffer.

## Slide 22
CONCLUSION
In summary, the project successfully integrates hardware, communication protocols, data processing algorithms, and cloud-based storage for a comprehensive ECG monitoring system. It holds potential applications in preventive healthcare and personalized fitness tracking.
Moving forward, the project could enhance signal processing with machine learning, broaden compatibility with different ECG devices, and improve the user interface.

## Slide 23
CHALLENGES
Detection of R Peak: Ensuring accurate detection of R peaks in ECG signals, especially in the presence of noise.
Calculation of BPM: Accurately calculating heart rate (BPM) from the detected R peaks while considering variable signal quality.
Live Data Display in Flutter Application: Achieving real-time data visualization in a Flutter application for a seamless user experience.
Sensor Issues: Addressing potential issues with the ECG sensor, such as signal artifacts or connectivity problems.

## Slide 24
THANK YOU